Equipment Program

Clinical Considerations for Prescribers
Traymobile

February 2013

Clinical Assessment

- Consider client’s upper limb strength, pain, consider amount of weight being put through traymobile, if using another form of walking aid, consider if a tray can be attached to their current frame.

- Note there is no weight tolerance for this item stated by the manufacturer – clients should not rely on this item for support.

- Traymobiles are contra-indicated for environments with steps and ramps as this equipment has no brakes.

- Consider the environment the traymobile will be used in, is the area congested and cause difficulties for the client.  Is the floor surface sufficiently smooth to prevent tipping and spills, some floor types may allow traymobile to “get away from client”.  Consider adding skids for these situations.

- Useful for rehabilitation activities.

- Client's cognitive ability to remember instructions.

Installation Considerations

- Height to be adjusted to should be specified by Physiotherapist or Occupational therapist, client should have elbows slightly bent when using.

- Client education should occur by PT or OT unless it is an exchange item.

- Check client is using the frame correctly, not too close or too far away when walking.

Client / Carer instructions

- Demonstrate and observe correct method of use and transfers using the equipment – gait pattern.

- Explain not to alter height once it has been adjusted

- Discuss limitations of tray on traymobile- ensure correctly placed on frame and weight of objects to be carried on tray

Safety and Review considerations.

Review – 12 monthly, as standard.  Review more frequently if client is weight bearing or mobilises awkwardly.

Checklist

- Is the item still in regular use and used as prescribed?

- Is this item still appropriate for the client? Do they need a more supportive aid?

- Still as prescribed, therefore at the correct height etc?

- All bolts or adjustment pins are functional and secure, adjustment holes round & not elongated

- Frame not excessively wobbly

- Wheels turn smoothly, no cracks