Equipment Program

Bed Rails

Clinical Considerations for Prescribers

October 2015

A bed rail is used to prevent falling/rolling out of bed.  There are potential risks (some of which are serious) associated with the use of bed rails and hazards related to the use of this equipment include:

- Parts of a person’s body can become trapped where there are gaps, for example between the rails of the bed rail, between the mattress and bed rail, between the mattress and bed-head/bed-end, between the end of the bed rail and the headboard/footboard

- The risk of suffocation if the person’s face is wedged against a soft surface (mattress or bed rail cover) restricting breathing

- Injuries from falls if the person climbs over the rails

- Injuries from falling or striking against the rails

A bed rail is NOT designed to help a person with bed mobility

Bed rails should only be considered after all other options to prevent rolling/falling out of bed have been eliminated (ie in exceptional circumstances)

Clinical Assessment Considerations

- To guide clinical decision making about whether bed rails are appropriate refer to the flowchart below. A clinical decision should then be made with the person/carer as to what solution is the lowest/least likely risk (ie bed rails, no bed rails or an alternative strategy).

- Document your clinical reasoning and decision in clinical notes

- Before providing bed rails ensure you have assessed alternative options to prevent falling/rolling out of bed. Many people can be safe in their beds without the use of rails. Other options to consider include:

  - Consider the need for a medical review (medication affecting sleep/settling, skin integrity, nutrition, pain management, circulation, etc)

  - Ensure needs are anticipated (e.g. drinks are accessible, regular toileting, call bell to hand)

  - Using tucked in sheets and blankets

  - Lowering an electrically height adjustable bed close to minimum height for sleeping (use caution where person can independently transfer)

  - Placing a floor mat or mattress next to the bed if the person is at risk of falling out of bed

  - Providing a foam mattress with firm or raised edges / concave mattress or bumpers

  - Provision of a positioning device or system

  - Use of monitoring systems/sensor alarms/alarm devices

  - Increased supervision when in bed

  - Using a ultra low adjustable bed

  - Using a larger bed

- In some situations the above options may not work for an individual person. The use of bed rails should only be considered after all other options have been eliminated. When using bed rails always consider that anywhere a gap exists could be a potential hazard. The most common areas for gaps to exist are between:

  - Rails of a bed rail

  - Bed rail and mattress

  - Bed rail and bedhead or bed end

  - Bed rail and clamp-on bed stick (where used together)

- Only prescribe bed rails suitable for the bed type: i.e. adjustable beds (bed rail will generally clamp on or need to be screwed into place) vs non-adjustable beds (bed rail may slide under the mattress)

- To guide clinical decision making about a person’s level of bed entrapment risk, refer to the “Guide to Assessing Entrapment Risk”. The level of bed entrapment risk will then guide the  decision about the need to assess bed entrapment zones:

  - Low Risk: assessment of entrapment zones is not required

  - Moderate/High/Extreme Risk: assessment of entrapment zones must occur

- To guide assessment of bed entrapment zones refer to “Bed Entrapment Zone Measuring Tool” as well as the “Instructions for  Measuring Entrapment Zones”

- Be aware that some people may be at risk of climbing over the bed rails. A person may be at higher risk of this if they are significantly confused, and have enough strength and mobility to climb over the rails. Younger people may be at risk as their mobility develops

- Consent needs to be provided by the person and/or carer for the supply of bed rails, as these are deemed a restrictive practice

- All paediatric clients require full length bed rails and covers

Bed Rail Covers

- If the person is at risk of entrapment bed rail covers may be considered to eliminate gaps between the rails. Ensure that the length of the bed rail covers cover the bed rail adequately to comply with bed entrapment zone guidelines and/or ensure person/carers have been instructed in correct positioning and placement of bed rail covers if there are gaps

- Be aware that a person could injure themselves on the bed rails. Consider padded bed equipment options. People may be more likely to knock the bed rails if they:

  - Are confused

  - Are showing signs of agitation or challenging behaviours

  - Do not understand the risks and/or their limitations

  - Have epilepsy

  - Have involuntary movements or muscle spasms

  - Have a sensory impairment

  - Are unable to alert others

- Bed rail covers can be fabricated from a variety of materials. Consider mesh for ventilation and padding where the client is at risk of knocking the bed rails

- Bed rail covers need to be firm fitting as lateral play in the covers or loose fixture points could enable a person to push against them and create a gap. Consider whether covers need to be removed to raise and lower rails and ease of doing this.

Precautions/Recommendations

- Where possible use bed rails and mattresses made to go with the bed and of a good fit

- Regularly check bed rails to ensure that they are securely attached and haven’t become loose

- If using bed rail covers, ensure they are firm fitting

- Avoid using pillows or cushions to fill gaps as they may be highly compressible and not fit the space well

- Avoid using bed rails to move the bed as this may loosen the rail attachments

- Avoid using bed rails as a grab rail support when standing

- Avoid using bed rails as a re-positioning aid

- A bed rail (for non-adjustable beds) can be placed on top of a bed board if the bed frame has wooden slats or sprung frame. Non-slip matting may be used to assist with keeping the bed rail in place.

- For bed rails that slide under the mattress, ensure sufficient weight is placed upon the bed rail to limit its movement while the user is in bed.  Person and mattress weight may be a consideration in prescription

Installation Considerations

Must be installed by trained staff

Person/Carer instructions

- Instruct person/carer to check the bed rail DAILY to ensure no gaps have been created. Gaps can pose a risk of trapping parts of the body and causing injury

- Instruct person/carers in monitoring of equipment and to report any issues with equipment safety and integrity

- Instruct person/carers to check bed rail covers are positioned appropriately and fastened securely when placed on bed rails.

- Educate carer(s) on use of the bed rail (i.e. lowering/raising the bed rail with safe manual handling techniques and ensuring the bed rail is locked into position)

Review

Every 12 months (as standard) and more frequently if the person has a progressive condition, or if the following changes occur, a person’s:

- Condition deteriorates

- Cognition decreases

- Changes to medication are made, with significant side effects

- Communication ability decreases such that person can no longer make needs known

- Unintentional movements increase

- An entrapment incident occurs

- Carer availability decreases

Check that:

- Equipment is still in place, in use and appropriate for the person

- Bed entrapment risk level assessed and assessment of entrapment zones occurs as required

- Person/carer given information sheet; “Bed Rail Fact Sheet”

Are bed rails appropriate?                                              See decision making flowchart on next page…