Background

In Australia there are presently no specific legal requirements surrounding which types of wheelchairs can or cannot be used in a vehicle. These prescriber notes look at some of the considerations for transportation of a wheelchair and occupant in a vehicle to support user safety.

This document aims to support clinicians in making recommendations to a client about the safest and best solution for their situation. However, a clinician must use their clinical judgement and reasoning, in conjunction with assessment tools and risk assessment when determining the best outcome. It is the client’s right to make an informed decision about their circumstances and any decisions to not comply need to be clearly documented.

The safest way for any person to travel in a vehicle is using the seat and seatbelt fitted by the vehicle manufacturer. However, some clients are unable to transfer from their wheelchair into the vehicle seat due to the level of their disability or need for postural support. If a client (or their carer) indicates that they intend to travel in a vehicle while seated in the wheelchair, the prescriber should discuss all the risks and options before determining if this is appropriate.

Note: If a client has an existing wheelchair that has not been crash tested, DHS will only replace this at the time that the chair either no longer meets the client’s significant functional and/or postural needs, or due to maintenance issues.  DHS will however modify the wheelchair to reduce the risk to the client i.e adding headrest.

- Clinical Considerations

- How does the client transfer?

  - If it is possible and safe for the client to transfer from their wheelchair into the vehicle seat and wear the seatbelt, this is the best option.

  - Consider the difficulty and risks associated in making the transfer.

  - Are there any other equipment items that may assist with this transfer? (e.g. handy bar or swivel seat)

- Consider the person’s postural and other medical needs or behavioural issues that may be compromised if the person is transferred into the vehicle seat.

- Ensure that all options are exhausted prior to considering transport within the wheelchair.

- If the client cannot transfer out of the wheelchair, consider:

  - What type of wheelchair does the client have?  Chairs have different configurations, and different tie down points for attaching wheelchair restraints

  - What type of vehicle(s) does the client intend to travel in? Different vehicles may require different methods of wheelchair restraint (see section 3)

  - How frequently are they travelling in the vehicle?

  - What is the impact of the recommendations on the clients safety and function?  Risk assessment needs to be completed.

2. Safety Considerations

- Wheelchairs used as a seat in a vehicle should have a backrest to the height of the top of the shoulder, a headrest fitted, be occupant crash tested and have tie down points.

- The person should be positioned so they are facing the front of the vehicle.

- It is best to ride with the backrest positioned at an angle of 30 degrees or less from the vertical.

- Accessories should be secured

- Any accessories that are loose or protrude from the footprint of the wheelchair should also be removed and secured preventing them from becoming loose projectiles in a vehicle impact.

- There are approved compartments that can be fitted to the car for this purpose available from after market vehicle storage manufacturers.

- A cargo barrier is recommended for station wagons.

- There is a clear space requirement of 650 mm in front of the client where a lap-sash belt is used and this is increased to 950 mm where a lap only belt is used, as well as 400 mm behind the head. Refer to AS/NZS 3696:19 for further information.

- Wheelchairs showing signs of rust or deterioration may no longer be suitable for transportation. Contact DES to arrange a maintenance check and report.

Crash testing and tie downs

- Some wheelchairs have been occupant crash tested in specific configurations and under particular conditions related to the standard it has been tested against.  If a chair is modified, this will usually alter the validity of testing.  Client weight, backrest height, headrest and configuration of seating and wheelchair will affect the wheelchair’s performance in an impact.

- Some chairs have tie down points but this does not necessarily mean that the chair has been occupant crash tested.

Prescribing headrests

- Wheelchair headrests are not designed to provide head restraint in a rear impact, and therefore, may not provide total head and neck protection. However, evidence from some studies and the principles of biomechanics indicate that a whiplash injury will be decreased when a headrest is used, and positioned correctly behind the back of the head.

- The headrest is fitted to a spreader bar on the back canes of the chair. Depending on how the headrest is fitted, the chair may no longer be able to be folded.

- When prescribing a headrest, consideration must be given to the following:

  - height of MWC backrest

  - client’s measurement to top of shoulder

  - height of installation of headrest above the MWC backrest

  - height of cushion

  - potential loss of ability to fold chair

  - impact on self propelling

- Ensure that the head position is within 50mm from the back of the head

- The centre of the headrest must be at least as high as the rear most point of the occupant’s head (generally the occipital prominence or in line with top of ear)

3. Wheeled mobility device & restraint types suitable for motor vehicle seating

In addition to the above considerations, please refer to the specific item information below:

Scooters Not currently tested to standards and unable to comply with clear space requirements in front of the person. Clients should not travel in a vehicle while seated in a scooter.

Adult Postural Chairs/ Air Tilt Chairs Ensure the chair meets Australian standards and has passed crash testing as most are not designed for this purpose. Consider how they are restrained in the vehicle.

Strollers Generally not suitable for transport when occupied.  Children should be transferred to an approved child safety seat when possible. Some strollers have been crash tested and may be suitable for transportation.

Type 1 (folding) If a person uses a Type 1 Manual Wheelchair, it is expected that they will transfer into the vehicle’s seat, except in exceptional circumstances when all other options for transportation have been exhausted.

Type 2 Manual Wheelchairs (folding) Contact DES to find out which wheelchairs have been crash-tested.

Type 3 Manual Wheelchairs (rigid frame) In most cases, the backrest on this type of wheelchair is too low and without the required headrest to safely transport a person seated in this type of wheelchair in any van, modified car or access cab. The wheelchair area on buses and trains is usually fitted with a rigid padded backboard and the person can travel safely in a rearwards facing direction with their back against this backrest.

Type 4 Manual Wheelchairs (Tilt in space) Contact DES to find out which wheelchairs have been crash-tested.

Type 1 Powered Wheelchairs (folding) These wheelchairs are generally unsuitable to be safely restrained with an occupant.

Types 2-4 Powered Wheelchairs Consult the supplier or DES at the time of prescription about the appropriate tie-down points on the wheelchair.

4. Restraint of the wheeled mobility device and occupant

- A load (including wheelchair and occupant) should be secured to the vehicle floor according to the Australian/ New Zealand Standard 3696:19 Wheeled Mobility Devices for use as seats in motor vehicles

- Note: The DHS Equipment Program does not provide vehicles or modifications to vehicles to put a wheelchair and occupant in a vehicle and does not provide wheelchair occupant restraint systems.

Securing the occupant

- Any lap belts or other harnesses fitted to the wheelchair as part of the seating are not suitable for transportation purposes and are not designed to be vehicle restraints. An approved wheelchair occupant restraint system fitted to the vehicle must be used regardless of whether any postural supports are in place.

Securing the chair

- Only approved restraint systems should be used. Never use untested straps such as those purchased from a hardware store as tie-downs. These may look the same as other vehicle tie-down straps but the load rating is likely to be insufficient to secure a wheelchair and occupant in the event of an impact.

- If the client has their own vehicle with a restraint system fitted, they should consult the supplier of the restraint system on the appropriate way to secure the new wheelchair.

- Does the wheelchair being considered have indicated tie-down points?

- New wheelchairs must have tie-down points labelled with tie-down instructions

- If not indicated, wheelchair should be secured by main frame, not removable parts such as leg rests or footplates. If not labelled, advice must be sought from the supplier or DES on location of appropriate tie down points on the wheelchair.

- Ensure that all people who may assist transporting the person in their wheelchair are made aware of the tie-downs and how to access information on the safe use of both the wheelchair and the wheelchair occupant restraint system in the vehicle being used i.e. from the relevant suppliers.

- Where a client is unable to be restrained in the vehicle as required by Australian Standards, the client or carer should contact the Department of Planning, Transport and Infrastructure on 1300 882 248 to discuss transport options. In some circumstances, a letter of exemption from a GP has been permitted after discussions with DPTI.

6.  Standards and Regulations

Australian/NZ Standard 3696:19 Wheeled Mobility Devices for use as seats in motor vehicles

AS/NZS 10542:4 Technical Systems and Aids for the Disabled

AS/NZS 10542:5

Transport Taxi Cabs Regulations 2008

Australian Road Rules

7. Other information and References

- Transport Safety Guidelines for People with a Disability -  TRANSPORT NSW

- Safe transportation of People with Disabilities – Robert Bingham, Rehabilitation Engineering Unit, Royal Perth Hospital

- Guidance on the Safe Transportation of Wheelchairs – Medical Devices Agency, UK

- Guidelines for Use of Secondary Postural Devices by Wheelchair Users During Travel in Motor Vehicles – RERC on Wheelchair Transportation Safety, USA