Domiciliary Equipment Service

Applying a Plastic Sheet Over Electrical Outlets - Fact Sheet

Photocopied versions may be outdated. See DES website for current version 						December 2013

When clients are showered outside of a shower alcove, additional precaution may be required to prevent water splash from entering power outlets, light switches and other electrical devices in the bathroom.

Instructions for using the sheet and tape:

- Tape A 600 x 600mm plastic sheet against the wall with the socket positioned under the centre of the sheet.

- A single line of tape across the top of the sheet is adequate.

- Blue (low adhesive) masking tape should be used on painted walls to decrease risk of paintwork being damaged.  Take care when peeling off the tape.

- White (regular) masking tape should be used on tiled walls.

- The area should be cleaned before applying the tape to the sheet and wall.

- The sheet should be removed following completion of the shower.

A sticker reading “Cover before showering” should be placed on the switch or power outlet as a reminder to use the sheet and tape.

Domiciliary Equipment Service      Phone:1300 295 786  Fax:1300 295 839   Email: equipment.feedback@dcsi.sa.gov.au

# Text boxes

Tape along top edge of sheet

600 mm

Plastic Sheet

Cover Before Showering

600 mm